SIGNIFICANT RULE CHANGES FOR 2015

3.1	Solar Car Divisions:  Classic, Open, Advanced, Electric-Solar Powered Car

5.2.3		Solar cars with a split shell outer-body covering must have double roll bars to

deflect the upper shell over the driver in the event that the shells separate during

a collision.

5.4.4(b)	The low battery warning system must be wired in series with the other

components of the supplemental system.

5.4.5		Solar cars must have two external and two internal cut off switches (as provided

within the rest of this rule)

5.12.1(a)	Stop lights must be red.  Turn indicators and Hazard lights must be amber.

5.12.1(b)	Stop lights must be visible at 100 meters.

5.12.1(c)	Stop lights must be pedal activated by both primary and secondary braking

systems.

5.12.1(e)	On cross-country races, both chase vehicles must be equipped with four amber

ECCO warning lights, model 3510 or 3518.

5.13(b)		Teams with body shells are required to have the shells attached to each other

to reduce the threat of injury during a collision.

5.13(j)		Solar car seats must be attached to the main structural frame using at least

grade eight bolts.

7.8		Teams working on their solar cars in the garage area must use protective

eyewear.  [Also found in Rule 24.13]

8.3	Fees – Registration for the Solar Car Challenge must be accompanied by a non-refundable $800 fee on February 1st of the year the team plans to participate.  Teams supplying a complete mechanical drawing of their solar car on June 1st will receive $100 back at Team Check-in; Teams supplying a complete electrical schematic of their solar car on June 1st will receive $100 back at Team Check-in;  Teams supplying Manufacturers’ Data Sheets for both their batteries and solar cells on June 1st will receive $100 back at Team Check-In.

In effect, the registration fee does not increase from the 2014 level. Teams are encouraged to provide the required registration materials “on time.”

8.5		Team guests are required to follow the same safety guidelines as the team.

8.7	Driver Weight.  No ballast is required in the Classic, Open, or Advanced Divisions.  A ballast requirement is set out in the Electric-Solar Powered Car Division.  [Rule 32]

10.1.1	The solar cell efficiency for the Classic Division has been increased to 19%.

[This also affects the solar cell efficiency for the Open Division, Rule 10.1.2]

10.1.3	Teams using lithium battery packs must have battery protection monitored

at the cell level.

10.1.4	ELECTRIC-SOLAR POWERED CAR DIVISION – The Electric-Solar Powered

Car Division provides teams the opportunity to build a two-seater electric vehicle

powered by a stationary power station.  This vehicle must meet all relevant

requirements set out for a Classic Division Car.  [See Section 32 for specifics]

19.2.2.9	No more than 3 support vehicles can travel within a mile of the solar car.

24.13		Teams working on their solar cars in the garage area must use protective

eyewear

32		Rules for the Electric-Solar Power Car Division  [See Addendum]

The two passenger requirement for the new Electric-Solar Powered Car Division mandates that the passengers must be seated “side-by-side” in the car.