## Slide 1: Specialty Workshop
Solar Car Challenge

## Slide 2: Levels of Participation
  Classic
  Veteran Classic
  Advanced
  Solar-Electric

## Slide 3: Classic Division
Solar cells less than 19% efficient
No hub motors
Lead/Acid Batteries
2018 Classic Division Champion: Solar Cats

## Slide 4: Advanced Classic Division
Same as Classic Division
*New*: Teams participating more than 2 years
2018 Advanced Classic Division Champion: Iron Lions

## Slide 5: Advanced Division
Solar cells limited by cell cost
Any Motor
Any battery chemistry
Use of University body molds is allowed
2018 Advanced Division Champion: Houston Solar Race Team

## Slide 6: Electric-Solar Powered Division
19% Solar Cell Efficiency
No hub motors
Two-person vehicle
Pb-Acid (2 packs x 2Kw.h)
Separate Charging Station
2018 Electric-Solar Powered Division Champion: All Saints

## Slide 7: Specialty Workshop
Building the Vehicle Frame

## Slide 8: Getting your car rolling
Building the Vehicle Frame
  Materials
  Roll bar and Crush Zones
  Suspension and Steering
  Wheels and Brakes

## Slide 9: Material for the frame
Steel
  Mild/Carbon Steel
    Really easy to work with (MIG welding)
    Inexpensive (<$1/foot)
    Heavy
    Can be easily changed/modified
    Readily accessible
    Comes in a large variety of sizes and wall thicknesses

## Slide 10: Material for the frame
Steel
  Chromoly Steel
    Harder to weld (requires TIG welding)
    More expensive ($4/foot) (+welding wire @ $15/lb)
    Light weight
    Can be easily changed/modified
    Comes in a large variety of sizes and wall thicknesses

## Slide 11: Material for the frame
Aluminum
  Very stiff for its weight
  Harder to weld (requires TIG welding)
  Needs more material to resist fatigue

## Slide 12: Material for the frame
Wicks Aircraft www.wicksaircraft.com
  Aluminum and 4130 Chromoly in a lot of size choices
Online Metals www.onlinemetals.com
  Titanium and a variety of plastics and metals

## Slide 13: Material for the frame
Carbon Fiber (composites)
  Lightest and stiffest
  Can be formed to any shape
  Expensive
  Needs careful planning
  Learning curve is steep
  Very hard to repair on the side of the road
  Need professional engineer certification if used for roll cage, roll bar, or crush zone

## Slide 14: Material for the frame
  Composites: Carbon fiber, resins, vacuum bag materials, and core materials

## Slide 15: Roll Bar and Crush Zone
Roll cage must:
  encompass the entire driver
  be integral part of the structure
  be designed to deflect body/array panels away from the driver
  allow 5 cm of clearance between the driver and the roll cage
  meet minimum diameter and wall thickness rules

## Slide 16: Roll Bar and Crush Zone

## Slide 17: Roll Bar

## Slide 18: Roll Bar
Front View
Side View

## Slide 19: Roll Bar and Crush Zone
Crush zone must:
  be designed to absorb impact from a collision
  protect the driver from front, side, and rear collisions
  have a minimum of 15 cm of horizontal distance from all parts of the driver’s body
  Teams must be able to demonstrate a specific, adequate crush zone in order to compete. Insufficient regard for structural safety will result in disqualification.

## Slide 20: Crush Zone

## Slide 21: Crush Zone

## Slide 22: Specialty Workshop
Wheels, Brakes, Suspension

## Slide 23: Wheels
One of the most difficult parts to source
Choices need to be made very early in the design process

## Slide 24: Wheels
  Four wheel designs
    More parts means higher cost
    Harder to get alignment correct
    Weight distribution less critical
    Much safer in the event of a flat
    Can “straddle” dead animals on the road

## Slide 25: Wheels
Wheel choices (must be able to handle the weight of the car and lateral forces from turning)
  NGM wheels and tires
  Motorcycle
  Junior Dragster
  Bicycle

## Slide 26: Wheels

## Slide 27: Wheels
Summit Racing www.summitracing.com
Universal Cycles www.universalcycles.com
Local motorcycle boneyard or ebay.com

## Slide 28: Brakes
Solar car must have two, independent, braking systems that allow the driver to stop the vehicle safely and quickly.
  Most cars use hydraulic disk brakes
    MCP single caliper brakes are easy to install and relatively inexpensive.
    BMI Karts www.bmikarts.com

## Slide 29: Brakes

## Slide 30: Brakes
Brakes are tested both statically and dynamically at the event.
Many vehicles have brake problems . Brakes must be tested before you arrive at the event!

## Slide 31: Suspension
Suspension systems
  More important on the road than on the track
  Adds weight and complexity to the vehicle
  Protects sensitive and expensive solar and electric parts

## Slide 32: Suspension

## Slide 33: Alignment
Suspension design and alignment have a huge effect on vehicle performance and handling.
Adding adjustability is worth the added weight.
Alignment should be checked everyday!

## Slide 34: Alignment
ATV A-Arm Suspension
www.ebay.com
Chassis Shop
www.chassisshop.com
FOX
www.ridefox.com

## Slide 35: More Details on Suspension/Steering

## Slide 36: Specialty Workshop
Powering the Solar Car

## Slide 37: Powering the solar car
How do you get the car moving?
  Photovoltaic array choices
  Power trackers and DC-DC converters
  Electric motors and controllers

## Slide 38: Shape of Array
Flat Solar Arrays
  Easier to execute
  Angle to sun less of a concern
Curved Solar Arrays
  Higher the angle the greater chance for breaks without ideal support.
  Angle to sun more of a concern

## Slide 39: The Solar Array
Pre-made panels
    Reliable
    Easily purchased
    HEAVY (glass front adds weight)
    www.wholesalesolar.com
    www.civicsolar.com

## Slide 40: The Solar Array
Premade or Custom Lightweight Options
SBMSolar.com

## Slide 41: The Solar Array
Raw cells and lamination
  Planning has to start FAR in advance (you are probably too late already!)
  Process is expensive
  Panels are very light and can be built to fit your car
  Easy to maximize power and reduce aerodynamic drag
  Sun Cat Solar Allen Chuzel Elgin, Arizonia
    (602) 710-0477

## Slide 42: Laminated Cells

## Slide 43: The Solar Array
Do-it-yourself solar array
  Amazing learning experience
  Learning curve is steep
  Hard to find raw cells  work with SunPower directly
  Takes a lot of manpower
  Hard to watch when cells are continually breaking
  Can fit exactly to your car

## Slide 44: Do-it-yourself

## Slide 45: Do-it-yourself

## Slide 46: MPPT and DC-DC Choices
AERL (Australian Energy Research Laboratories) www.aerl.com.au
Solar Converters Inc
Outback (and other grid type MPPTs) www.midnightsolar.com
DC-DC Converters www.kellycontroller.com
Genasun www.genasun.com

## Slide 47: AERL MPPTs

## Slide 48: Low Voltage Indicator
Do-It-Yourself kit available at:
http://store.qkits.com/
Look for “Low Voltage Alarm”

## Slide 49: Electric Motors
Brushed Electric Motors
  Inexpensive
  Lower overall efficiency
  Controller is inexpensive and easy to wire
Brushless Electric Motors
  Very efficient
  More expensive
  Controller is more difficult to wire (typically 3 phase)

## Slide 50: Brushed Motor Examples
  Briggs and Stratton ETEK
  Lynch LM200
  PMG 132 Perm Motor
  Cloud Electric www.cloudelectric.com
  Electric Motorsport www.electricmotorsport.com
  Thunderstruck Motors www.thunderstruck-ev.com
  Robot Market Place www.robotmarketplace.com

## Slide 51: Brushed PWM Controller
Alltrax AXE
Easy to wire
0-5k Pot control
Programmable
Durable

## Slide 52: Brushless Motor Example
Motenergy ME0907 Brushless PMSM/BLDC www.evdrives.com
Revolt http://www.revolt.org.il

## Slide 53: Hub Motor
NGM ‘Direct Drive’ high efficiency in-hub motor with variable air gap adjustment.
  Super efficient over a broad range of speeds
  No need for gears or chain
  Very expensive (Motor + controller > $25,000)
Mitsuba / Nomuri hub motors replacing NGM as favored motor for solar car teams
  Still ~$25,000

## Slide 54: Electrical System
Main electrical system (the one that makes your car move)
  Use the correct gauge wire for the job
  Disconnect switches should be designed for DC
  Fuses
Secondary electrical system (everything else on your car)
  Lights
  Fans
  Horn

## Slide 55: Electrical System Layout

## Slide 56: Electrical System Layout
Schematic made with:
http://www.digikey.com/schemeit/
Or use Solid Edge to set schematic (can get wire lengths)

## Slide 57: Electrical System

## Slide 58: Batteries
Choose carefully young padawan!
Batteries are one of the areas where you get what you pay for.
  Decisions to make:
    What voltage does your car run at?
      Higher voltage means lower current (smaller wires)
    How much weight can you carry?
    How much energy can you get at that weight?
    Can your solar panels recharge the battery pack?
    Is it a road race or a track race?

## Slide 59: Batteries
The 5 kilowatt-hour rule
  kw-h = Amp-hours x Voltage
  (at the 20 hour discharge rate)
  Example:
  Four, 12 volt, 84 amp-hour batteries in series
  84ah x 48 v = 4032 watt-hours or 4.032 kilowatt-hours
  (this battery pack would weigh around 230 pounds)

## Slide 60: Batteries
Some of our favorites:
  Concorde Sun Xtender series
    84 Ah $245/battery www.wholesalesolar.com
  EnerSys Odyssey Marine series
    68 Ah $250/battery
Lithium Batteries Battery Space www.batteryspace.com

## Slide 61: Batteries
Choosing batteries based on the Peukert number:
  A typical sealed lead acid battery has a Peukert number between 1.1 and 1.3. (The closer to 1.0 the better!)

## Slide 62: Batteries
Testing batteries:
  Understanding how your batteries perform is one of the most important things you can know BEFORE the race starts.
  Carefully recording voltage, current, and amp-hours will help your team make good decisions during the race

## Slide 63: Lights/Turn signals
    Low-draw LED lights are easy to find.
    Etrailer www.etrailer.com
    Grainger www.grainger.com (ECCO lights)
    O’Reilly Auto Parts www.oreillyauto.com

## Slide 64: Switches/Fuses
    There are a lot of resources for switches and fuses. Be sure they meet the race requirements before ordering!
    Be sure they are rated for your DC system. (AC rating will not qualify!)
    (Bussmann FWH Fuses are rated at 500V DC)
    Electric Motorsport www.electricmotorsport.com
    Tecknowledgey
    http://www.tecknowledgey.com
Single Pole On/Off Rated load: 400 A Break Current: 1200 A @ 48 V DC (600 A @ 96 V DC)
500V DC @90 amp fuse is about $50

## Slide 65: Specialty Workshop
Power Management

## Slide 66: Power Management
How much power does it take to make your car go down the road?
  The amount you will use depends on:
      Aerodynamic drag
      Rolling friction
      Weight
      Electrical system resistance

## Slide 67: Power Management
A typical Solar Car Challenge vehicle array produces 800-1000 watts of power.
There is approximately 12 hours of usable sunlight during a race day.
800 watts x 12 hours = 9600 watt-hours of energy/day. (Assuming clear skies and good sun.)
A full-size, fully-charged battery pack has approximately 4000 watt-hours of energy.
It will take approximately 5000 watt-hours of energy to completely recharge the battery pack.

## Slide 68: Power Management
Dead Batteries are dead weight
  A 48 volt battery pack is “dead” at 42 volts.
It will take (at least) 5 hours of full sun to completely recharge a dead battery pack.
Hills, clouds, trees, wind, and children with sticky fingers all reduce your array efficiency.
The only way you will know how much energy your car will use is to test it.
Keep a record of current draw vs. mph (It is not linear!)

## Slide 69: Strategic Decisions
First step in power management is deciding your high-level strategy (without looking at numbers)
  Do you empty your battery pack each day and recharge as much as possible during off-hours?
  Do you end the day with as much energy as you can recover during off-hours?
  Do you run down a certain capacity each day so you end up with no energy left on the last day (e.g. run down ¼ of pack each day for 4 day event)?
Do you run based on net draw (motor – solar) or motor draw?
No right answers; just decisions the team must make

## Slide 70: Set Targets Based on Strategy
If strategy is to empty battery pack each day, and you have a 100 Ah battery pack, how fast should the driver drive?
  Trick question: Driver does not drive based on speed, but current draw.
OK, how much current should driver be taking from the battery?
  100 Ah / 6 hours of racing (Classic Division) = 16.7 A, right?
Classic Division runs 9am-12pm, 2-5pm, with 2 hours lunchtime in between. How much charge will I get back during the two hours?
  Assume 1000W panel, 48 V system = ~20 A  40 Ah
  After 3 hours of racing at 16.7A, would have (100Ah – 16.7A x 3 hrs = 49.9Ah)
  After 2 hours of charge time, 49.9 Ah + 40 Ah = 89.9 Ah left
  Rest of racing period = 89.9 Ah / 3 hrs = 30 A
To get the same current draw throughout the day, what should the current draw be?
  100 Ah + 40 Ah = 140 Ah / 6 hours = 23.3 A

## Slide 71: Collecting Data
How to measure what your car is doing:
  Voltmeter and/or ammeter
  Batman measurement system (Bruce Sherry Design)
  Link (e-meter)

## Slide 72: What Data is Important?
Different teams have different answers to this!
Typical measurements include:
  Battery Voltage (measured under load)
  Motor current draw (the rate that you are taking energy out)
  Array current (the rate that you are putting energy back in)
  Amp-hours or Watt-hours (how much total energy you have taken out or put back in)

## Slide 73: What’s Interesting About This Data?

## Slide 74: Charging Characteristics
Power stays fairly constant throughout racing period (~1000 W)
Power input drops near end of charging period (takes more power to fill pack)
Battery voltage remains fairly stable, even when current changes (because of MPPT)

## Slide 75: What’s Interesting About This Data?

## Slide 76: Discharge Characteristics
Current draw is not directly correlated to speed; associated with acceleration
Wide range of current draw for specific speed, including outliers

## Slide 77: How Do I Get The Right Data
Test! Test! Test!
Multiple runs at different speeds
Test both uphill and downhill (at different grades)
Simulated race days

## Slide 78: Making Decisions

## Slide 79: Getting Data to the Right People
Driver should not need to make decisions other than driving.
Pit crew should inform driver about “speeding up” or “slowing down”.
One person should be responsible for communicating with the driver.
Telemetry systems

## Slide 80: Choose the Correct Gears
Don’t gear a car for 50 mph if you are going to drive it at 25 mph. Be realistic about your cars speed!
Chain drive systems can be very efficient if gears are aligned and lubricated.
Pictured: 48V system, 15 tooth front, 70 tooth rear. Max speed = 36 mph

## Slide 81: Choose the Correct Gears
Custom Sprockets:
Rocket Sprockets www.rocketsprocket.net
PMP Sprockets www.pmpsprocket.com

## Slide 82: Other Power Management Considerations to Research & Test
How does weather affect charging?
How much power do you get at different angles of sun?
How does different array shapes/angles affect charging?
How does the route topology (or track layout) affect power usage?
Other Considerations?

## Slide 83: Specialty Workshop
Aerodynamics & Friction

## Slide 84: Rolling Resistance
Bearings can be opened, cleaned, and filled with a light oil.
Tires with thin “supple” casings roll better than thick casings. (Higher risk of flats)
Fat tires roll better than thin tires. (But weigh more.)
If it rotates: lubricate!
Wheel alignment is critical to reducing rolling resistance.

## Slide 85: Aerodynamic Drag
Reducing drag is the least expensive way to improve your solar car.
The extra weight of drag reducing fairings is easily made up for in aerodynamic efficiency.

## Slide 86: Shrink Wrap Body Cover
Made from 7-mil shrink-wrap that is used to protect boats in the winter.
Shrink-wrap is cut to shape and taped to the car with inexpensive tape that is made for the material.
A common heat gun can be used to shrink the material.
The material cools and maintains a semi-rigid surface.
Easily repaired with tape.

## Slide 87: Cut and Tape the Material

## Slide 88: Reinforce and Heat

## Slide 89: Trim to fit around fairings
Shrink Wrap
Big Shrink www.bigshrink.com
Comes in a variety of colors and thicknesses

## Slide 90: Specialty Workshop
Solar Car Challenge