## Slide 1: Station 2 Electrical Scrutineering Common Issues & Good Practices
Liam Hubbard, Chief Electrical Judge
SCC 2018-Present

## Slide 2: Station 2 Intent
Ensure a minimum level of electrical systems safety
Ensure Rules Compliance
Improve Car Electrical Reliability

## Slide 3: Common Issues that will keep your team from passing station 2:
High Voltage in Driver Compartments
Lacking or non-matching documentation of critical systems
Unsecured wires and components
Uninsulated wires, connections, components
Electrical tape as high voltage insulation
Missing Locking fasteners on high voltage
Driver entrapment issues from hanging wires during egress
Improperly Rated Components
Incorrectly Wired Disconnect Switches
Unable to Verify Documentation Matches Components

## Slide 4: How to check your car before getting to the race so you can go do other things instead of station 2:
Perform a mock inspection of your own car and be very strict on your car with respect to the rules
If you don’t think something will pass, fix it, or send an email to the race for a rule's clarification, much easier to fix it before the race than during.
Example: When checking the insulation of the high voltage, if hypothetically someone could drop a wrench across it and short something, it probably needs better insulation.