## Slide 1: Building the Vehicle Frame
Chris Jones, Chief Race Judge

## Slide 2: Building the Vehicle Frame
Materials
Safety Cell, Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 3: Material for the frame
Mild/Carbon Steel
  Really easy to work with (MIG welding)
  Inexpensive (~$2/foot)
  Heavy
  Can be easily changed/modified
  Readily accessible
  Comes in a large variety of sizes and wall thicknesses

## Slide 4: Material for the frame
Chromoly Steel
  More expensive (~$12/foot) (+welding wire @ $15/lb)
  Light weight
  Can be easily changed/modified
  Comes in a large variety of sizes and wall thicknesses

## Slide 5: Material for the frame
Aluminum
  Very stiff for its weight
  Harder to weld (TIG)
    MIG is possible, but not wire-fed
  Generally tubular; notch to get better fit
  Needs more material to resist fatigue
  Can be difficult to repair

## Slide 6: Material for the frame
Titanium
  Light
  Strong (but not stiff)
  Absorbs shock
  Hard to weld
  Expensive
  Limited sizes

## Slide 7: Material for the frame
Carbon Fiber (composites)
  Lightest and stiffest
  Can be formed to any shape
  Expensive
  Needs careful planning
  Learning curve is steep
  Very hard to repair on the side of the road
  Need professional engineer certification if used for safety cell, roll bar, or crush zone

## Slide 8: Building the Vehicle Frame
Materials
Safety Cell, Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 9: Safety Cell, Crush Zone, Roll Bar
Safety Cell (previously Roll Cage) – rigid protection encompassing entire driver; minimum OD of 1.9cm; minimum 5cm clearance to driver; minimum coverage
Roll Bar – protects driver in event of rollover; continuous piece of metal; minimum 5cm vertical clearance; minimum OD of 5cm; minimum wall thickness based on material; welded to frame
Crush Zone – structural components designed to collapse on impact; minimum 15cm clearance to outside of safety cell; minimum height for left/right crush zone

## Slide 10: Safety Cell Structure
15cm
15cm
15cm
15cm
Safety Cell encompasses driver’s head, torso, legs, feet
Minimum height for left/right side crush zone = 30cm

## Slide 11: Crush Zone
Crush zone must:
  be designed to absorb impact from a collision
  protect the driver from front, side, and rear collisions
  have a minimum of 15 cm of horizontal distance from the outside of the safety cell
Teams must be able to demonstrate a specific, adequate crush zone in order to compete. Insufficient regard for structural safety will result in disqualification.

## Slide 12: Safety Cell / Roll Bar / Crush Zone Good Example
Crush Zone structure – thin material designed to collapse on impact
Safety Cell – rigid protection encompassing entire driver
Roll Bar – continuous piece of metal; protects driver in event of rollover
Safety Cell Coverage – If wrapped in elastic fabric, no part of driver should touch fabric (other than arms holding steering wheel)

## Slide 13: Safety Cell / Roll Bar / Crush Zone Example
Crush Zone structure – may not meet 15 cm
Safety Cell – rigid protection encompassing entire driver
Roll Bar – continuous piece of metal; protects driver in event of rollover
Safety Cell Coverage
(in orange)

## Slide 14: Roll Bar Example
Front View
Side View
Continuous piece of metal
Sufficient vertical clearance (5 cm between head and underneath of bar)
Material OD is less that what the rules specify but a waiver was granted
USE THE WAIVER PROCESS (RULE 5.21)

## Slide 15: Roll Cage / Crush Zone Example
Safety Cell – good use of strong structural components; needs additional coverage for driver torso
Crush Zone – would prefer structure less rigid and deflect away from driver
This is one dimensional and would not pass current rules

## Slide 16: Building the Vehicle Frame
Materials
Safety Cell, Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 17: Suspension Design
Agenda
Purpose of Suspension
Suspension components
Types of Suspension
Basic Suspension Geometry
Steering Geometry

## Slide 18: Suspension Purpose
Minimize shock to the driver and the car
Enhance car stability while traveling on dynamic terrain
  Keep the Tires on the Ground
  Seriously, Your tires are the only connection the car has to the ground

## Slide 19: Suspension Components
Spindle
Hub
Axle
Tie Rod

## Slide 20: Common Front Suspension Types
Solid Axle
MacPherson Strut
Dual A Arm
Notes: MacPherson
-production vehicles
-tend to be heavy
-limited adjustability
Solid Axles
-simple
-geometry is set at construction
-can be heavy
Double Arm
-most popular
-very versatile
-can be complicated with lots of options and area for mistakes

## Slide 21: Common Front Suspension Types
 | Macpherson | Solid Axle | Double Wishbone (Dual A-Arm) | No Suspension
Pros | Less Components Easier to build | Simple Inexpensive Easy to manufacture | Versatile Most popular (Easy to find parts) Most Adjustability | Less weight Less components Easy to make
Cons | Limited Adjustability Heavy Undesirable Handling | Heavy Poor ride quality | Complicated (lots of areas to make mistakes) Difficult to manufacture | Rough on other components Require Strong Chassis(& Driver) Will fail on road race

## Slide 22: Some Tips about Suspension
Lets pause for a second…
Suspension Can be very complex
  Don’t Fall into the rabbit hole!
  Design for Strength
  Design for Adjustability if possible

## Slide 23: Suspension Geometry
Rear/Front View
  Camber
Vertical
Negative
Vertical
Front
Positive
Affects grip and stability in cornering
Not applicable to solar car racing

## Slide 24: Scrub Radius
Scrub Radius
Positive
Harder to Turn
Increase wear on tire
Positive
    Cause center seeking
Notes: How much force/wear for turning
Coffee cup experiment – turn cup by turning on a point vs. turning using the handle
Minimize the scrub radius to lessen energy

## Slide 25: Caster (Side view)
Front
Vertical
θ
Creates straight line stability
Positive Caster
  Steering wheel feedback
  Makes car harder to turn
  Causes wheels to self center
Negative Caster
  Unstable
Positive
Notes: No correct answer; need to set it up for the driver

## Slide 26: Toe Geometry (Top View)
Center Line
Front
Center Line
Center Line
Neutral
In
Improves straight line stability
Out
Improves Steering Response
Can make steering “jerky”
Notes: Toe
Affects Tire Wear: want to run straight down the road – if in/out, will drag
Solar cars – affected by use of thin tires (Bridgestone Ecopia)

## Slide 27: Measuring Toe
A1
A2
B1
B2
Front
C
Dist A
Dist B
Notes: How to do proper alignment
Measure at the same spot each time

## Slide 28: Suspension/Steering Considerations
Steering Axis
  Line between two pivot points of the wheel

## Slide 29: Ackerman Steering

## Slide 30: Getting your car rolling
Building the Vehicle Frame
  Materials
  Safety Cell, Roll bar and Crush Zones
  Suspension and Steering
  Wheels and Brakes

## Slide 31: Wheels
One of the most difficult parts to source
Choices need to be made very early in the design process
Three wheel designs:
  Lighter
  Easier to align
  Less expensive
  Not as safe

## Slide 32: Wheels
Four wheel designs
  More parts means higher cost
  Harder to get alignment correct
  Weight distribution less critical
  Much safer in the event of a flat
  Can “straddle” dead animals on the road
Required for Cruiser Division

## Slide 33: Wheels
Wheel choices (must be able to handle the weight of the car and lateral forces from turning)
  NGM wheels and tires
  Motorcycle
  Junior Dragster
  Bicycle

## Slide 34: Wheels
Motorcycle
Jr Dragster
Jr Dragster

## Slide 35: Wheel Considerations
Weight
  High Polar Inertia designs have potential for increased energy consumption
    Extreme example is a flywheel
  Affected by acceleration
Solid vs. Spokes
  Solid = better aerodynamics, may weigh more
  Spokes = worse aerodynamics, less load capacity
  Can be improved by wheel fairings

## Slide 36: Tire Considerations
Tire Width
  Thinner = less rolling resistance
  Thicker = supports more weight and more stable on road
Contact patch
  Minimize Contact patch = Minimize Energy loss (less rolling resistance)
  Tire deforms where it contacts the road
Ideal
Patch
Side
Real
Patch
Side

## Slide 37: Brakes
Solar car must have two, independent, braking systems that allow the driver to stop the vehicle safely and quickly.
  Most cars use hydraulic disk brakes
  MCP single caliper brakes are easy to install and relatively inexpensive.

## Slide 38: Brake Pedals
Brake pedals must also be independent
  Pedals, master cylinder, etc. separate for each system
Can no longer “link” pedals together
Must be operated by foot (no hand brakes)
Automotive style pedals must be used
X

## Slide 39: Brake Testing
Brakes are tested both statically and dynamically at the event.
  Static = Test strength of brakes at rest
  Dynamic = Test how fast brakes can stop car
Many vehicles have brake problems. Brakes must be tested before you arrive at the event!

## Slide 40: Building the Vehicle Frame
Chris Jones, Chief Race Judge